Just replace the OID in netapp.dta file ( 7 Mode devices ) or in netapp_cmode.dta file ( C Mode devices ) and restart the probe. Reopen the probe GUI and you will see the change.

E.g. How to change Interface Operational Status OID in netapp.dta file :

a.      Here is the contents for Interface Operational Status from netapp.dta file ===

<Operational Status>

unit = State

CIType = 5.1.4.3

CIMetric = 18

desc = The current operational state of the interface. The testing(3) state indicates that no operational packets can be passed. Syntax  INTEGER {up(1), down(2), testing(3), unknown(4), dormant(5), notPresent(6), lowerLayerDown(7) }

<NetApp>

type = 2

<oids>

<1>

lookup_base_table_disc = .1.3.6.1.2.1.2.2.1.2

match_string = $instance

lookup_base_table_value = .1.3.6.1.2.1.2.2.1.2

oid = .1.3.6.1.2.1.2.2.1.8.X

</1>

</oids>

</NetApp>

</Operational Status>

OID getting used is .1.3.6.1.2.1.2.2.1.8.X.

b.      If customer is having other OID as .1.3.6.1.2.1.2.2.1.9 to get the operational status then just replace it and new contents will be :

<Operational Status>

unit = State

CIType = 5.1.4.3

CIMetric = 18

desc = The current operational state of the interface. The testing(3) state indicates that no operational packets can be passed. Syntax  INTEGER {up(1), down(2), testing(3), unknown(4), dormant(5), notPresent(6), lowerLayerDown(7) }

<NetApp>

type = 2

<oids>

<1>

lookup_base_table_disc = .1.3.6.1.2.1.2.2.1.2

match_string = $instance

lookup_base_table_value = .1.3.6.1.2.1.2.2.1.2

oid = .1.3.6.1.2.1.2.2.1.9.X

</1>

</oids>

</NetApp>

</Operational Status>

c.      Save the netapp.dta file and close it.

d.      Restart the probe and you will see the new OID in probe GUI.