## 3Com

### Steps for 802.1x configuration

Note: The following configuration is based on model “3COM 4400 3C17206 24 ports”, OSI version 5.00.

- Use “CONSOLE” or “TELNET” to connect to the swich, then log in as “admin”.

The diagram below shows the CLI interface:

Choose“gettingStarted”from the main menu to setup IP address for the switch:

RADIUS configuration:

  - Choose “security” from the main menu:

  - Enter “radius”:

  - Enter “authentication”:

    - Enter LAN Enforcer IP address in “Primary authentication server IP address”

    - Enter “1812” in the “Primary authentication server UDP port number”. This should match with the enforcer settings in SEPM.

  - Enter“SharedSecret” to input the shared secret between the switch and RADIUS；

  - Enter “quit” to go back to the main menu

EAP configuration on ports:

- Enter“network”，then“access”, as shown on the diagram below:

- Enter“portsecurity”for 802.1X settings. To set the 2nd port on the first row, enter “1：2”，see diagram below:

- Enter “quit” to go back to the main menu.

VLAN configuration

  - Enter “bridge”, then “vlan”, as shown as the diagram below：

  - Default Vlan is the default vlan on the switch, and its VLAN ID is 1. To create a new vlan, enter  “create”, diagram below create vlan3, with VLAN ID 3

  - Enter“summary” gives a list of vlan created

d.	Enter ”modify”, then “addport”to add a specific port into a specific vlan. For example, add port“1：5” to vlan 3:

e. 	Enter “detail”will give you a list of vlans with their associated ports

## Foundry

### Sample configuration

Current configuration:

ver 03.3.01cTc1

no global-stp

no spanning-tree

dot1x-enable

re-authentication

timeout quiet-period 30

timeout re-authperiod 30

mac-session-aging no-aging permitted-mac-only

enable ethe 8 to 24

aaa authentication dot1x default radius

ip address 192.168.100.253 255.255.255.0

ip default-gateway 192.168.100.1

radius-server host 192.168.100.90 auth-port 1812 acct-port 1813 default key 1 $RZ+|n8U3 dot1x

radius-server timeout 30

interface ethernet 8

dot1x port-control auto

interface ethernet 9

dot1x port-control auto

interface ethernet 10

dot1x port-control auto

interface ethernet 11

dot1x port-control auto

interface ethernet 12

dot1x port-control auto

interface ethernet 13

dot1x port-control auto

interface ethernet 14

dot1x port-control auto

interface ethernet 15

dot1x port-control auto

interface ethernet 16

dot1x port-control auto

interface ethernet 17

dot1x port-control auto

interface ethernet 18

dot1x port-control auto

interface ethernet 19

dot1x port-control auto

interface ethernet 20

dot1x port-control auto

interface ethernet 21

dot1x port-control auto

interface ethernet 22

dot1x port-control auto

interface ethernet 24

dot1x port-control auto

end