Resolving APM CE Business Transaction “Sudden Increase” Issues

Version .01a February 13th 2015

Preview Draft --  Comments Appreciated!

Hallett German

Principal Support Engineer

CA Technologies

Hallett.German@ca.com

Table of Contents

- Introduction

- Guiding Principles

- Out of Scope

- Factors Impacting Sudden Increase in Transaction Counts

- How to Resolve

- Acknowledgements

1. Introduction

This tech note supplements “Resolving APM CE Business Transaction/Defect Count Issues” that was created both as a Tech Tip and a Tech Note.

Transaction/Defect counts is a particular issue that takes time to research. This Tech Note covers a particular count issue. The scenario is the following:

- Looking at the Performance Reports and Transaction Trend Reports, the transaction count/total transactions have suddenly increased between time periods. This is typically between two days, weeks, or months.

Versions:

.01 Preview Version. Publically distributed for review.

2. Guiding Principles

- APM CE (also called CEM) attempts to create consistent and complete statistical/defect reports.

- Various non-product factors can cause dramatic increases in transaction counts. These are listed below.

3. Out of scope

The following is out of scope for this document:

- Dramatic decreases across time periods. In many cases, this will be due to the opposite of those factors listed below.

- Other transaction count issues.

4. Factors Impacting Sudden Increase in Transaction Counts

These product and non-product factors can cause a sudden increase in APM CE (CEM) transaction counts.

| Factor | Possible Recent Change | How it Impacts |
| --- | --- | --- |
| Network Traffic Filters | Network connection to TIM or MTP reconfigured to see traffic from additional networks. | May pick up additional transactions from new networks. |
| Network quality (packets being lost, out of order, retransmitted) | Network infrastructure changes and upgrades. | Transactions are incomplete or missing due to network quality issues. This increases the number of defects and the number of total transactions. |
| SSL factors (cipher suites, TLS versions and features) | A new private key was added. | More successful decodes potentially leading to a higher transaction count. |
| Transaction definitions changed | Transaction definition becomes broader. (Such as going from /foo/foo to /foo.) It also could be that a new application release came out that is impacting the count. | Transaction counts are higher than expected due to broader definition resulting in more matches. |
| Ambiguous definitions | Adding a second environment that uses same URL. | Successfully matching on the same URL for a second environment could mean more transactions. |
| Retention Period | Changes in retention period. | Changes the number of active defects. |
| Incomplete Data | Not receiving all the data. | For example, day one has all 24 hours but day two has only 12. So this would appear as a sudden drop. |

- How to Resolve

| Factor | What to do |
| --- | --- |
| Network Traffic Filters | Verify with the network team has changed filters allowing more traffic from additional networks. |
| Network quality (packets being lost, out of order, retransmitted) | Review Network infrastructure changes and upgrades to restore network quality, |
| SSL factors (cipher suites, TLS versions and features) | Determine if a new private key was added. Then analyze whether before or after the change is the correct transaction count/decode failure rate. |
| Transaction definitions changed | Make transaction definitions more restrictive. Determine if a new application release came out. |
| Amiguous definitions | Add matching on hostname or request/response variable showing environment. (Such as Prod, Test, or QA.) |
| Retention Period | Review changes in retention period. |
| Incomplete Data | Review if comparing two timeframes with complete data. |

6. Acknowledgements

Credits & Acknowledgements

- Thanks to Tom Wyszomierski, Leonardo Anez, and Gnanawathy Hareendran for bringing this to my attention and discussing in our weekly APM queue review meeting.