### How to create a custom startup WinPE 2.x-3.x CD with SEE Full Disk Access or SEE Recover Utilities support

### I. SEE Full Disk Access

- Install the Windows Automated Installation Kit (Windows AIK). You can download the Windows AIK from one of the following links:

Windows Automated Installation Kit (AIK) for Windows 7 (WinPE 3.0)

http://www.microsoft.com/downloads/en/details.aspx?familyid=696DD665-9F76-4177-A811-39C26D3B3B34&displaylang=en

Automated Installation Kit (AIK) for Windows Vista SP1 and Windows Server 2008 (WinPE 2.1)

http://www.microsoft.com/downloads/details.aspx?familyid=94BB6E34-D890-4932-81A5-5B50C657DE08&displaylang=en

Windows Automated Installation Kit (AIK) (WinPE 2.0) http://www.microsoft.com/downloads/details.aspx?FamilyID=C7D4BC6D-15F3-4284-9123-679830D629F2&displaylang=en

Note: Different Windows AIK versions should not be installed on same machine/OS.

- Create a folder on your hard disk named <build_location> (for example c:\buildwpe).

- Open the Windows PE Tools Command Prompt from Start->Programs->Microsoft Windows AIK->Windows PE Tools Command Prompt.

- At the command prompt, run the Copype.cmd script. The script requires two arguments: hardware architecture and destination location.

Example:

copype.cmd <arch> <arch_destination>

Where <arch> can be x86, amd64, or ia64 and <arch_destination> is a path to the local directory.

Example:

copype.cmd x86 c:\buildwpe\winpe_x86

The script creates the following directory structure and copies all the necessary files for that architecture.

Example:

\winpe_x86 \winpe_x86\ISO \winpe_x86\mount

- At the command prompt, mount the base Windows PE image (Winpe.wim) to the \mount directory by using ImageX.

Example:

imagex /mountrw c:\buildwpe\winpe_x86\winpe.wim 1 c:\buildwpe\winpe_x86\mount

- If you want to add additional drivers, such as network card drivers, run the following:

peimg /inf=<path> c:\buildwpe\winpe_x86\mount\Windows

Where <path> is path to the inf file of the driver.

Example:

peimg /inf=c:\dell\drivers\e6500\e1y6032.sys c:\buildwpe\winpe_x86\mount\Windows

If you want to additional drivers, for each other driver after the first run:

imagex /apply c:\buildwpe\winpe_x86\winpe.wim 1 c:\buildwpe\winpe_x86\mount peimg /inf=<path> c:\ buildwpe\winpe_x86\mount\Windows

- Edit the file startnet.cmd located in the <arch_destination>\mount\Windows\System32 folder, and add the following content to this file:

@echo off

wpeinit

%SYSTEMDRIVE%\Utilities\SEEFD_Access_Utility

- Copy the files ephdxlat.sys and eafsprot.sys to the

<arch_destination>\mount\Windows\System32\drivers folder.

Next, copy the files

mfc80.dll,

mfc80u.dll,

mfcm80.dll,

mfcm80u.dll,

msvcm80.dll,

msvcp80.dll,

msvcr80.dll,

Microsoft.VC80.CRT.manifest,

Microsoft.VC80.MFC.manifest,

SEEFD_Access_Utility.exe,

EPCL32.dll,

EAECCWinPE.dll,

EAFRWinPEDBWrapper.dll,

EAFRWinPEUserManagement.dll,

EAHDWinPEDBWrapper.dll,

EAHDCliSectAccEAFS.dll, and

EACaseConverter.dll

to the <arch_destination>\mount\Utilities folder.

These files are available in the Utilities folder of the Full Disk download package.

- Register the drivers in the WinPE SYSTEM file. Run regedit.exe (under Windows XP or Windows Server 2003) or regedt32.exe (under Windows 2000).

- Click on HKEY_LOCAL_MACHINE.

- From File -> Load Hive, load the \mount\Windows\System32\config\ SYSTEM file.

- Expand the key HKEY_LOCAL_MACHINE\Temp\ControlSet001\Control\Class\{4D36E967-E325-11CE-BFC1-08002BE10318}

- Double-click on the registry value UpperFilters and add an ephdxlat entry.

IMPORTANT: When adding the ephdxlat entry, make sure that you do not enter any leading or trailing spaces in the name.

- Open the HKEY_LOCAL_MACHINE\Temp\ControlSet001\Services and create a new key named EPHDXLAT with following string and double word values:

| Key Name | Type | Value |
| --- | --- | --- |
| DisplayName | String Value (REG_SZ) | GuardianEdge Encryption Filter |
| Group | String Value (REG_SZ) | PnP Filter |
| ErrorControl | DWORD Value (REG_DWORD) | 0x00000001 |
| Start | DWORD Value (REG_DWORD) | 0x00000000 |
| Type | DWORD Value (REG_DWORD) | 0x00000001 |

- Open the HKEY_LOCAL_MACHINE\Temp\ControlSet1\Services and create a new key named EAFSPROT with following string and double word values:

| Key Name | Type | Value |
| --- | --- | --- |
| EpfsVolumePath | String Value (REG_SZ) | <without value> |
| Group | String Value (REG_SZ) | filter |
| ImagePath | String Value (REG_SZ) | System32\drivers\eafsprot.sys |
| ErrorControl | DWORD Value (REG_DWORD) | 0x00000001 |
| ProtectionStyle | DWORD Value (REG_DWORD) | 0x00000001 |
| Start | DWORD Value (REG_DWORD) | 0x00000000 |
| Type | DWORD Value (REG_DWORD) | 0x00000002 |

- Click on HKEY_LOCAL_MACHINE\Temp and unload the hive using File -> Unload Hive.

- Commit the changes to the original image file (Winpe.wim) by using the ImageX /unmount option with the /commit option.

Example:

imagex /unmount /commit c:\buildwpe\winpe_x86\mount

- Replace the default Boot.wim in the \ISO directory with your new custom image. The image must be called Boot.wim.

Example:

copy /y c:\buildwpe\winpe_x86\winpe.wim c:\buildwpe\winpe_x86\ISO\sources\boot.wim

- Create an .iso file with Oscdimg. At the command prompt, type:

oscdimg –n -b<arch_destination>\etfsboot.com <arch_destination>\ISO <arch_destination>\<iso_filename>.iso

Example:

oscdimg -n -bc:\buildwpe\winpe_x86\etfsboot.com c:\buildwpe\winpe_x86\ISO c:\buildwpe\winpe_x86\winpe_x86.iso

This creates a no-emulation bootable (-betfsboot.com) ISO image with long file name support (-n).

- Burn a CD with the c:\buildwpe\winpe_x86\winpe_x86.iso image you just created.

IMPORTANT: Do not place the access utility and the recover utility on the same Windows PE CD as they are not compatible and functionality issues may occur as a result.

II. SEE Recover

- Install the Windows Automated Installation Kit (Windows AIK). You can download the Windows AIK from one of the following links:

Windows Automated Installation Kit (AIK) for Windows 7 (WinPE 3.0)

http://www.microsoft.com/downloads/en/details.aspx?familyid=696DD665-9F76-4177-A811-39C26D3B3B34&displaylang=en

Automated Installation Kit (AIK) for Windows Vista SP1 and Windows Server 2008 (WinPE 2.1)

http://www.microsoft.com/downloads/details.aspx?familyid=94BB6E34-D890-4932-81A5-5B50C657DE08&displaylang=en

Windows Automated Installation Kit (AIK) (WinPE 2.0) http://www.microsoft.com/downloads/details.aspx?FamilyID=C7D4BC6D-15F3-4284-9123-679830D629F2&displaylang=en

Note: Different Windows AIK versions should not be installed on same machine/OS.

- Create a folder on your hard disk named <build_location>(for example c:\buildwpe).

- Open the Windows PE Tools Command Prompt from Start->Programs->Microsoft Windows AIK->Windows PE Tools Command Prompt.

- At the command prompt, run the Copype.cmd script. The script requires two arguments: hardware architecture and destination location.

Example:

copype.cmd <arch> <arch_destination>

Where <arch> can be x86, amd64, or ia64 and <arch_destination> is a path to the local directory.

Example:

copype.cmd x86 c:\buildwpe\winpe_x86

The script creates the following directory structure and copies all the necessary files for that architecture.

Example:

\winpe_x86 \winpe_x86\ISO \winpe_x86\mount

- At the command prompt, mount the base Windows PE image (Winpe.wim) to the \mount directory by using ImageX.

Example:

imagex /mountrw c:\buildwpe\winpe_x86\winpe.wim 1 c:\buildwpe\winpe_x86\mount

- Edit the file startnet.cmd located in: <arch_destination>\mount\Windows\System32 folder, and add the following content:

@echo off

wpeinit

%SYSTEMDRIVE%\Utilities\SEERecoverWinPE

- Copy the SEERecoverWinPE.exe file to the

<arch_destination>\mount\Utilities folder.

This file is available in the Utilities folder of the Full Disk download package.

- Commit the changes to the original image file (Winpe.wim) by using the ImageX /unmount option with the /commit option.

Example:

imagex /unmount /commit c:\buildwpe\winpe_x86\mount

- Replace the default Boot.wim in the \ISO directory with your new custom image. The image must be called Boot.wim.

Example:

copy /y c:\buildwpe\winpe_x86\winpe.wim c:\buildwpe\winpe_x86\ISO\sources\boot.wim

- Create an .iso file with Oscdimg. At a command prompt, type:

oscdimg –n -b<arch_destination>\etfsboot.com <arch_destination>\ISO <arch_destination>\<iso_filename>.iso

Example:

oscdimg -n -bc:\buildwpe\winpe_x86\etfsboot.com c:\buildwpe\winpe_x86\ISO c:\buildwpe\winpe_x86\winpe_x86.iso

This creates a no-emulation bootable (-betfsboot.com) ISO image with long file name support (-n).

- Burn a CD with the c:\buildwpe\winpe_x86\winpe_x86.iso image you just created.